## Slide 1
FPGA Power Modeling
LMS Algorithm with Cost Function
Linear Power Modeling
Tool Flow
Motivation
Power dissipation is a major concern in computer system
Existing power analysis method
  RTL / gate-level simulation: extremely slow
  Cycle accurate software simulation: still slow
  Analytic modeling: not accurate
Goal: fast and accurate power analysis
Solution: FPGA-accelerated power analysis
  Generate the power model of selected signals
  Add counters for the selected signals
  Analyze the system’s power using signal activities from FPGA simulation
Donggyu Kim
Modeling Results
Future Work
Evaluate the power model for various benchmark
Develop the DRAM power model with counters in DRAM controller
Generate the counter structure
Evaluate FPGA simulation’s speed and accuracy
Chisel
Design
Backannotation
FPGA simulation
Design with Activity Counters
FPGA simulation
Gate-level
simulation
Chisel Verilog
Backend
DC & ICC
Gate-level design
RTL
Test-harness
Power Analysis
Power Model Generation
PrimeTime PX
Power Model Generator
Gate-level Power Estimation
Gate-level Switching Activities
RTL
simulation
RTL Switching Activities
Counter Structure Generator
Power Model
Given a sample (A, y), solve y = Ac where A = [x1 x2 … xn]T: transition matrix xt : switching activity vector at time t y = [e1 e2 … en]: energy vector yt : power consumption at time t
Linear regression with the LMS algorithm
Problem
  Switching vectors are not independent
  Need to reduce the model’s dimension (signal numbers to be watched)
Xt
Yt
T
Graphical Representation for Linear Power Modeling
Assign the cost functions for the signals
Select signals with the highest cost
Algorithm
  Let f(i) be the cost function of i’th signal
  Initialize f(i) = 0 and c(l) = 0
  Update f(i) = f(i) + [(Θ(l))i * (xt)i]
  Update c(l+1) = c(l) + ρ(yt – Θ(l)Txt)
Control Unit
Data Unit
I-Cache
D-Cache
Notes: Please put in notes here to explain poster so that someone else could summarize what your poster is about